## Slide 1: Major Source Air Permitting in Nonattainment Areas, or What’s an Offset?
Amy Browning, Texas Commission on Environmental Quality
{views expressed in this presentation are my own, and not necessarily those of the agency}

## Slide 2: Ozone Nonattainment Areas
2015 8-Hour Ozone
Houston-Galveston-Brazoria – Serious
Dallas-Fort Worth – Serious
Bexar County – Serious
2008 8-Hour Ozone
Houston-Galveston-Brazoria – Severe
Dallas-Fort Worth – Severe

## Slide 3: 2010 SO2 Nonattainment Areas
Portions of the following counties:
Freestone and Anderson Counties
Howard County
Hutchinson County
Navarro County
Rusk and Panola Counties
Titus County

## Slide 4: 2024 PM2.5 Nonattainment Areas
None currently

## Slide 5: Requirements for Major Source Permitting in Nonattainment Areas
LAER – Lowest Achievable Emission Rate
Offsets for permitted emissions

## Slide 6: What are Emission Offsets? (from EPA)
Offsets are emission reductions, generally obtained from existing sources located in the vicinity of a proposed source which must (1) offset the emissions increase from the new source or modification and (2) provide a net air quality benefit. The obvious purpose for requiring offsetting emissions decreases is to allow an area to move towards attainment of the NAAQS while still allowing some industrial growth.
https://www.epa.gov/nsr/nonattainment-nsr-basic-information

## Slide 7: What emissions are subject to offsets?
Ozone
  No direct emissions of ozone
  Precursor emissions that form ozone – NOX and VOCs
  Environmental contribution
Other pollutants
  Direct emissions as well as precursors
  PM2.5 – NOX, SOX, and potentially ammonia as well as the PM2.5 itself

## Slide 8: What’s an environmental contribution?
Required for offsets in ozone nonattainment areas.
Emissions in excess of the allowable emissions that are required as an offset.
Ratios from the Federal Clean Air Act.
Increase with increasing severity of the nonattainment designation.

## Slide 9: Ratios for ozone
Marginal: 1.1 to 1: 100 tons needs 110 tons
Moderate: 1.15 to 1: 100 tons needs 115 tons
Serious: 1.2 to 1: 100 tons needs 120 tons
Severe: 1.3 to 1: 100 tons needs 130 tons
Extreme: 1.5 to 1: 100 tons needs 150 tons

## Slide 10: Why does it matter?
Allows new construction or major modification of major projects in nonattainment areas while still allowing progress to attainment.
Emissions must be removed from the airshed to account for emissions from major projects.

## Slide 11: Where do they come from?
Reductions in real, actual emissions that are included in the State Implementation Plan (SIP) emissions inventory that are permanent, enforceable, quantifiable, and surplus.
Generated in a current nonattainment area.
Sometimes - Allowances used for cap and trade programs for specific pollutants in certain areas may also be used for offsets.

## Slide 12: Rules – 30 TAC Chapter 101, Subchapter H
ERCs – Emission Reduction Credits
MECT – Mass Emission Cap and Trade program for NOX in the HGB nonattainment area
HECT – Highly Reactive VOCs Emission Cap and Trade Program for certain VOCs in Harris County
DERCs – Discrete Emission Reduction Credits

## Slide 13: ERCs – Emission Reduction Credits
30 TAC § 101.302(d)(1) – a certified emission reduction that:
  Must be enforceable, permanent, quantifiable, real, and surplus;
  Must be surplus at the time it is created, as well as when it is used; and
  Must occur after the SIP emissions year for the facility.

## Slide 14: Important deadlines to consider when generating credits
60-month lifespan – runs from the time of the emission reduction.
Some oil and gas facilities – 72-month life span in certain circumstances.
2 years to generate credits from the time of the emission reduction strategy.

## Slide 15: PM2.5 – new challenges
PM2.5 itself.
Precursors: NOX, SOX, and potentially ammonia.
Can only generate ERCs in a designated nonattainment area.

## Slide 16: Questions
Further information - https://www.tceq.texas.gov/airquality/banking/erc_program.html
Amy Browning, amy.browning@tceq.texas.gov