## Slide 1: Adventures in PFAS (Crazy) Candy Land
August 8, 2025
Kirby Tyndall, PhD, DABT
Senior Associate Toxicologist
PFAS Session
Everlasting Gobstoppers

## Slide 2: Just How Crazy is PFAS Candy Land?
National Primary Drinking Water Regulations (Maximum Contaminant Levels; MCLs)
CERCLA designation
Proposed RCRA Listing
TSCA Reporting Requirements
Biosolids Risk Assessment
Draft Human Health Ambient Water Quality Criteria
National Ambient Water Quality Criteria (aquatic life)
TRI Reporting for Additional PFAS
…Add your personal favorite
Likely that number of publications will increase throughout 2025
Increase in PFAS Publications over Time

## Slide 3: Evolving Science, Regulations, Awareness
From: PFAS and Biosolids: What Wastewater Pros Need to Know | California Water Environment Association
PFAS | Final MCL (ppt)
PFOA, PFOS | 4.0
PFNA, PFHxS, GenX | 10
Final Regulatory Determination for MCLs
  PFOA/PFOS MCLs at Practical Quantitation Limit
  Hazard index of 1 for mixtures of PFNA, PFBS, Gen-X, PFHxS
  Five years to comply (2029)
  Contain NEW non-cancer and cancer toxicity values
  Underlying tox values are used for other risk-based regulations

## Slide 4: No Consensus Opinion on PFOA/PFOS Exposure & Association or Causation of Adverse Health Outcomes
Human studies show
associations with…
Effects on immune system
Elevated cholesterol
Decreased birth weight
Cancer (“likely”)
“limited or no evidence for any causal link… and any human disease”
“The available epidemiological studies suggest associations … ; however, cause-and-effect relationships have not been established…“
“…no evidence for a link between exposure to PFASs and cancer risk.”
vs.
PFOA = “carcinogenic to humans”
PFOS = “possibly carcinogenic to humans”

## Slide 5: Why the Inconsistency?
1. Inconsistent Science Interpretations
Selection of Key Studies (Animal Bioassay or Human Epidemiology)
Selection of Critical Endpoint
Point of Departure in exposure-response relationship
Uncertainty Factors
Drinking Water (MCLs)
Surface Water (AWQCs)
Risk-based Screening Values (RSLs)
Fish Advisories
2. Regulatory Program/Policy
Human Health Toxicity Assessment for Perfluorooctanoic Acid (PFOA) | US EPA
One of many decisions made related to choosing endpoint of concern with epi (18 health systems), animal (15 health systems) and mechanistic data and evaluating quality of study.

## Slide 6: Controversy Exists for All Human Health Endpoints
Inconsistent data
True “adversity” of endpoints
Reverse causation and/or confounding
Source: The Logic of Science Available: https://thelogicofscience.files.wordpress.com/2016/01/hierarchy-of-evidence2.png
Largely negative and/or weak
Human relevance uncertain
Inconsistent, chance of bias/confounding

## Slide 7: Results of Inconsistency…
TCEQ is in the process of updating PFAS tox values and expect to issue draft for public comment/review by end of 2025.
Different science policy decisions
Very different interpretations of the PFOA/PFOS toxicity
Challenges with risk communication
Varying Regulatory Values

## Slide 8: What is the Real Risk to Humans from PFAS?
How will receptors contact the chemical?
What is the magnitude, frequency, and duration of contact?
What are the chemical’s harmful effects?
What is the relationship between dose level and health effects?
What is the likelihood of harmful effects in a population (including sensitive subpopulations)?
Risk = Toxicity x Exposure
Risk is the foundation for making decisions that protects public health and the environment
Toxicity is often used synonymously with hazard identification
Image generated by Copilot

## Slide 9: Navigating in PFAS Candy Land
Are PFAS A Problem?
It’s More Than Just PFOA/PFOS and Drinking Water
No Consensus on PFOA/PFOS Toxicity
Public health benefits of PFAS toxicity values are highly uncertain
Consumer Products
Dynamic Science and Regulations
  State legislation at forefront
Depends on which PFAS
Not all PFAS are the same
Depends on legal/regulatory paradigm
Due Diligence
Alternatives Assessments??
Property Redevelopment
  Unclear what actions EPA will take in near future
  Litigation trends setting precedent

## Slide 10: What Solutions Do We Have?
PFAS are not “forever chemicals”
“Assortment” of treatment technologies & approaches for PFAS are available
Significant advancements are being made in numerous fields
Destruction: Plasma
Concentration: Sorbents
Separation: Foam Fractionation
Destruction: Ball Milling
Destruction: Thermal Plasma
Destruction: Supercritical Water Oxidation

## Slide 11: THANK YOU
Kirby Tyndall, PhD, DABT
khtyndall@gsienv.com
Science · Strategy · Solutions